Oxford Hackspace Maintenance Schedule

Equipment / activity:	JAS Silvertail A0 Laser Cutter
Assessment conducted by:	Paul Riggs
Date of assessment:	16 November 2016
## Maintenance tasks
### Clean mirrors
Interval: 1 month
Dirt gradually accumulates on the mirrors, which causes them to absorb and scatter more laser energy, reducing the performance of the cutter. Extra heat in the mirrors can also lead to damage over time. To keep the mirrors clean, gently wipe them with a microfibre cloth and alcohol spray. Do this before the alignment process described below, as it can cause the mirrors to become misaligned. Please note that heavy use of the cutter may require the mirrors to be cleaned between the standard intervals.
### Check alignment
Interval: 1 month (after cleaning mirrors, or moving the cutter)
The laser alignment needs to be checked to ensure the machine’s accuracy, particularly at the extremes of its movement. This can be done by making small adjustments to the mirrors that guide the laser to its target.
You can check the alignment of each mirror by placing masking tape over entry point of the laser into the subsequent mirror along the beam path. Closing the laser cutter lid and briefly pressing the ‘laser’ button on the control panel will fire the laser, burning a hole in the tape. By adding a new layer tape, you can compare the laser entry point with the cutting head at different locations.
The position of each mirror is adjusted by loosening or tightening the screws behind it. If the beam is hitting the next mirror in the optic system too high, tighten the top screws very slightly and loosen the bottom screw very slightly. This will move the reflected beam down. To move the beam to the left, loosen the left top screw and tighten the top right one.
First, check the alignment of the beam entering the mirror on the left of the laser gantry. It should enter at the same point at both extremes of the gantry’s movement in the Y direction. If this is not the case, the first mirror, at the output of the laser tube, needs to be aligned.
Next, check the alignment of the left-hand mirror by checking its entry point to the final mirror at both extremes of its movement in the X direction.
Lastly, check the final mirror alignment by placing masking tape under the laser head. The burn should be a single point. Any burning in a partial halo around this point indicates the beam is reflecting off the inside wall of the laser nozzle rather than passing through it.
### Cleaning the cutter
Interval: 1 month (or after heavy use)
Debris from cutting jobs accumulates around the inside of the cutter and needs to be cleaned away. Pay particular attention to the areas around the tracks, where the machines movement can be obstructed, underneath the hex and knife beds, and in the floor of the machine enclosure.
Check that the top surface of the hex bed is free from any cutting residue that might affect its flatness, and wipe it clean if necessary.
### Checking the filtration system
The filters in the filtration system are consumable, and need periodic replacement. The system is designed to have a long life, but should be checked to ensure good performance. The stages of the filtration system are as follows:
- G4 paper panel pre-filter
- F8 rigid bag filter
- H13 HEPA filter
- Activated carbon cylinder filter (x16)
More information about replacing these filters is found on the OxHack wiki.
Signs of a filter needing replacement are:
- Reduced flow causing smoke to clear more slowly from the cutting area
- Build-up of debris on the filter surface
- Smell of cutting vapours in exhaust indicates the carbon filters need to be refilled
### Checking the cooling system
Interval: 1 month
The laser cooling system is low maintenance and fail-safe, but its water level should be checked periodically to pre-empt problems. This is done by removing the screw cap and checking the level with a dipstick.
Maintenance task	Date completed	Carried out by	Date next due	Notes