Oxford Hackspace Risk Assessment

Equipment / activity:	JAS Silvertail A0 Laser Cutter
Assessment conducted by:	Paul Riggs, based on earlier assessment by Tim Stephens
Date of assessment:	27 September 2016

What are the hazards?	Who/what harm may result?	What actions are being taken?	What further action is necessary?	Action by who?	Action by when?	Completed
Smoke / fumes in Hackspace and outside the building	Users / other persons present / passers by risk health damage from inhaling fumes and smoke	- Air filtration system is installed / - Users trained to use the filtration system correctly / - Users trained to delay opening cutter lid while smoke clears from cutting bed	- Observe life of filter media, formalise inspection and replacement schedule for filters	Tech.	20/12/2016
Hazardous fumes created when cutting inappropriate materials	Users / other persons present / passers by risk health damage from inhaling fumes and smoke	- Air filtration system is installed / - Users trained in which materials can be cut on the laser cutter	- Create database of safe materials and cutting parameters and make it available on the wiki	Tech.	20/12/2016
Failure of filtration system	Users / other persons present / passers by risk health damage from inhaling fumes and smoke	- Train users to be vigilant for problems with the filtration system
Fire starting on laser cutter bed	Risk of fire spreading to building	- Laser cutter must not be left unattended while running / - Users trained to follow this rule, staff actively ensure that it is followed / - Any incidents of sustained flames being spotted in the laser cutter must be logged / - Fire extinguisher is kept close to the cutter, notice indicates its location / - Cutter is cleaned regularly to avoid debris buildup, according to maintenance schedule	- Assess incident log and consider extra rules or restrictions as appropriate / - Assess whether maintenance arrangements are adequate and review as appropriate	Tech.	16/6/2017
Burning ember transferred to filtration system	Fire in filter enclosure, risk of fire spreading to building	- Fire safety precautions as stated above / - Design follows precedents set by industrial laser filter manufacturers	- Assess need for thermal cutout switch in filter housing to cut fan in event of fire	Tech.	16/6/2017
Water used to extinguish fire	Electric shock, damage to equipment	- Users trained not to use water to extinguish electrical fires / - Prominent safety notice	- Consider removing water extinguishers from vicinity of laser cutter / entire Hackspace	Tech.	16/6/2017
Powerful IR laser	Eye damage, burns	- Laser cutter is interlocked to prevent unsafe use / - Train users not to cut reflective materials	- Add baffle to prevent laser being visible through gaps around lid	Tech	16/6/2017
High voltage laser power supply	Electric shock	- Access panels are locked / - Maintenance only by competent technicians	None
Moving parts inside machine	Trapped fingers / clothing	- Train users to exercise caution when moving the laser gantry with the cutter lid open	None
Workpiece may be hot after cutting	Minor burns	- Train users to exercise caution when moving newly-cut pieces	None

### Training points
Items to cover in training for this machine, specific to the risk assessment:
Using the filtration system, awareness of problems that can develop, look for smoke flow
- Delay opening cutter lid while smoke clears
- Materials whitelist, ask for help with non-listed materials, don’t cut reflective materials
- Don’t leave cutter unattended
- Be aware of fire extinguishers, don’t use water or foam on electrical equipment
- Difference between harmless flames that follow the cutting path, and sustained flames needing intervention
- Log sustained fire incidents on the wiki
### Training checklist
Users should agree to the following points before being allowed to use the equipment.
- I have attended and understood the training provided for this machine
- I am competent using the machine, and will seek help with any aspects of its use I’m uncertain about
- I understand how to use the filtration system, and will be vigilant for any problems relating to its use
- I will not use any non-whitelisted materials in the machine without first discussing with a trainer
- I understand the risk of fire inherent to this machine, and how to respond appropriately
- I will report any sustained fires, accidents, or damage to the machine that occurs while I am using it
Risk assessment form derived from HSE guidelines: http://www.hse.gov.uk/risk/controlling-risks.htm
### Definitions
Hazard – thing that may cause harm
Risk – chance of harm arising from a hazard
### HSE 5 step risk assessment
1. Identify the hazards
2. Decide who might be harmed and how
3. Evaluate the risks and decide on precautions (Useful categories:)
  1. Eliminate / substitute (finding alternatives to avoid risk)
  2. Engineering controls (interlocks etc.)
  3. PPE
4. Record your significant findings
5. Review your assessment and update if necessary
### Initials
LH	Lauren Hutchinson
JL	Jamie Lokier
JR	Jared Reabow
PR	Paul Riggs
Tech.	Either of the two Hackspace technicians JR, PR