Hazard
Abbreviation
Hazard/Warning
Description / Location of Hazard
Mitigation

Laser
Contains Class 4 Laser.
Laser is interlocked with lid & will switch off if lid opens. Do not override interlock system.

High Temperature
Parts may be hot after cutting.
Do not touch parts immediately after cut.

High Voltage
Laser tube powered with high voltage supply.
Do not remove panels on the machine body whilst system is energised.

F
Ignition Source
Laser may ignite workpiece.
Do not leave machine unattended whilst operating. Remove dust and debris from bed.

Xi
Irritant
Smoke and fume may be generated during cutting operation.
Ensure ventilation active. Allow fumes to disperse before opening cover.

Fire Fighting and Environmental Hazard

Do not use water fire extinguisher.
Ensure ventilation system is turned on and operating prior to laser operation.

Power Supply and Shutdown Procedure

In the event of an emergency, equipment may be safely turned off at the wall sockets.
Emergency Contact Procedure

In the event of an emergency, speak to the technician or keyholder on duty.
Should they not be available, contact any of the individuals below.

Responsible User Details
Name
Mobile
Notes
Jared Reabow
07929 596 513
Oxhack Technician.
Jamie Lokier
07853 244 489
Oxhack Director. Lives nearby.
Lauren Hutchinson
07708 931 042
Oxhack Director. H&S / insurance lead.

Additional Information

Only Oxhack members who have passed the formal training induction may use this machine.
Anyone else needing a cut done should email prototyping@oxhack.org or phone the Oxhack technicians on 01865 261 462.
Only material that is explicitly included on the ‘safe materials’ list may be cut on this machine.
Machine must not be operated unattended.

Building & Room Number
OCFI , Room B8
Local Room Name
Laser Cutter Room
Department/
Division
Oxford Hackspace