Oxford Hackspace Risk Assessment

Equipment / activity:	JAS Silvertail A0 Laser Cutter
Assessment conducted by:	Paul Riggs, based on earlier assessment by Tim Stephens
Date of assessment:	27 September 2016

What are the hazards?	Who/what harm may result?	What actions are being taken?	What further action is necessary?	Action by who?	Action by when?	Completed
Smoke / fumes in Hackspace and outside the building	Users / other persons present / passers by risk health damage from inhaling fumes and smoke	- Air filtration system is installed / - Users trained to use the filtration system correctly / - Users trained to delay opening cutter lid while smoke clears from cutting bed	- Observe life of filter media, formalise inspection and replacement schedule for filters	Tech.	20/12/2016
Hazardous fumes created when cutting inappropriate materials	Users / other persons present / passers by risk health damage from inhaling fumes and smoke	- Air filtration system is installed / - Users trained in which materials can be cut on the laser cutter	- Create database of safe materials and cutting parameters and make it available on the wiki	Tech.	20/12/2016
Failure of filtration system	Users / other persons present / passers by risk health damage from inhaling fumes and smoke	- Train users to be vigilant for problems with the filtration system	None
Fire starting on laser cutter bed	Risk of fire spreading to building	- Laser cutter must not be left unattended while running / - Users trained to follow this rule, staff actively ensure that it is followed / - Any incidents of sustained flames being spotted in the laser cutter must be logged / - Fire extinguisher is kept close to the cutter, notice indicates its location / - Cutter is cleaned regularly to avoid debris buildup, according to maintenance schedule	- Assess incident log and consider extra rules or restrictions as appropriate / - Assess whether maintenance arrangements are adequate and review as appropriate	Tech.	16/6/2017
Burning ember transferred to filtration system	Fire in filter enclosure, risk of fire spreading to building	- Fire safety precautions as stated above / - Design follows precedents set by industrial laser filter manufacturers	- Assess need for thermal cutout switch in filter housing to cut fan in event of fire	Tech.	16/6/2017
Water used to extinguish fire	Electric shock, damage to equipment	- Users trained not to use water to extinguish electrical fires / - Prominent safety notice	- Consider removing water extinguishers from vicinity of laser cutter / entire Hackspace	Tech.	16/6/2017
Powerful IR laser	Eye damage, burns	- Laser cutter is interlocked to prevent unsafe use / - Train users not to cut reflective materials	- Add baffle to prevent laser being visible through gaps around lid	Tech	16/6/2017
High voltage laser power supply	Electric shock	- Access panels are locked / - Maintenance only by competent technicians	None
Moving parts inside machine	Trapped fingers / clothing	- Train users to exercise caution when moving the laser gantry with the cutter lid open	None
Workpiece may be hot after cutting	Minor burns	- Train users to exercise caution when moving newly-cut pieces	None

### Training points
Items to cover in training for this machine, specific to the risk assessment:
Using the filtration system, awareness of problems that can develop, look for smoke flow
- Delay opening cutter lid while smoke clears, beware hot items
- Materials whitelist, ask for help with non-listed materials, don’t cut reflective materials
- Don’t leave cutter unattended
- Be aware of fire extinguishers, don’t use water or foam on electrical equipment
- Difference between harmless flames that follow the cutting path, and sustained flames needing intervention
- Log sustained fire incidents on the wiki
### Training checklist
Users should agree to the following points before being allowed to use the equipment.
- I have attended and understood the training provided for this machine
- I am competent using the machine, and will seek help with any aspects of its use I’m uncertain about
- I understand how to use the filtration system, and will be vigilant for any problems relating to its use
- I will not use any non-whitelisted materials in the machine without first discussing with a trainer
- I understand the risk of fire inherent to this machine, and how to respond appropriately
- I will report any sustained fires, accidents, or damage to the machine that occurs while I am using it
Risk assessment form derived from HSE guidelines: http://www.hse.gov.uk/risk/controlling-risks.htm
### Definitions
Hazard – thing that may cause harm
Risk – chance of harm arising from a hazard
### HSE 5 step risk assessment
1. Identify the hazards
2. Decide who might be harmed and how
3. Evaluate the risks and decide on precautions (Useful categories:)
  1. Eliminate / substitute (finding alternatives to avoid risk)
  2. Engineering controls (interlocks etc.)
  3. Personal Protective Equipment (gloves, masks, goggles etc.)
4. Record your significant findings
5. Review your assessment and update if necessary
### Initials
LH	Lauren Hutchinson
JL	Jamie Lokier
JR	Jared Reabow
PR	Paul Riggs
Tech.	Either of the two Hackspace technicians JR, PR