Oxford Hackspace Risk Assessment

Equipment / activity:	Roland MDX-40 CNC Mill
Assessment conducted by:	Paul Riggs (based on earlier assessment by Tim Stephens)
Date of assessment:	4 July 2016

What are the hazards?	Who/what harm may result?	What actions are being taken?	What further action is necessary?	Action by who?	Action by when?	Completed
Electric shock whilst maintaining the equipment	Severe injury to maintenance personnel servicing machine	- Covers and guards fitted to all electrical systems. - Training log kept of qualified personnel. Servicing carried out by suitably trained personnel. Covers off work on non-electrical components to be carried out only when system isolated from mains. / - Servicing to be carried out only by suitably qualified personnel / - Covers off work to be carried out only when system isolated from mains.	None	PR	4/7/2016	4/7/2016
Cutting injury from spinning tool	Minor injury to users	- Interlock present on machine, brakes tool immediately if opened	None
Workpiece thrown from bed	Minor injury to users, bystanders	- Machine has interlocked cover; will not operate if cover is opened / - Users to be trained in correctly clamping workpiece	None
Tool breakage ejects parts at speed	Eye damage, minor injury to users, bystanders	- Machine has interlocked cover; will not operate if cover is opened	None
Workpiece / tool may become hot while operating	Minor burns to user	- Train users to expect hot parts and exercise caution	None
Dust from cutting operation	Irritation, potential adverse health effects to users and bystanders	- Dust extraction is provided / - Train users to use extraction whenever appropriate	None
Fumes from cutting operation	Irritation, potential adverse health effects to users and bystanders	- Harmful fumes not expected from normal use of the mill / - Train users to report incidents where fumes are noticable	- Evaluate whether any further mitigations around fumes are warranted.	Tech.	31/1/2017
Injury during set-up of machine for different operation (e.g. conversion to 4th axis)	Minor injury to users by dropping components on feet/hands, cuts etc.	- Only specifically trained users to be allowed to adjust tooling / - PPE is available as required	None
Use of mill by incompetent people	Injury to user	- Training is mandatory for all users of the mill / - Machine is interlocked and fitted with emergency stop button / - Young people must be mature enough to understand risks associated with tool use, and carefully follow safety instructions / - Minors to be allowed to use equipment only with supervision by adult trained in the use of the machine	None